## Slide 1: BCD and Gray CODE

## Slide 2
Outline
  Human Perception
  Binary Codes
  Decimal and BCD
  BCD Operation
  Gray Code

## Slide 3: Human perception
We naturally live in a base 10 environment.
Computer exist in a base 2 environment.
So give the computer/digital system the task of doing the conversions for us.

## Slide 4: Binary Codes
“An n-bit binary code is a group of n bits that assume up to 2n distinct combinations of 1s and 0s, with each combination representing one element of the set being coded”.
For the 10 digits need a 4 bit code. One code is called Binary Coded Decimal (BCD).

## Slide 5: Decimal and BCD
The BCD is simply the 4 bit representation of the decimal digit.
For multiple digit base 10 numbers, each symbol is represented by its BCD digit
Decimal Symbol | BCD Digit
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001

## Slide 6: BCD Operation
Consider the following BCD operation
  Decimal: Add 4 + 1
  Covert to binary 0 1 0 0
  And 0 0 0 1
  Getting 0 1 0 1
  Which is still a BCD representation of a decimal digit

## Slide 7: BCD Operation (cont.)
Another example
3 0 0 1 1
  +3 0 0 1 1
  Getting 6 or 0 1 1 0
  And in range and a BCD digit representation

## Slide 8: BCD Operation (cont.)
Another example
Consider 5 + 5
5 0 1 0 1
+5 0 1 0 1
giving 1 0 1 0 which is binary 10 but not a BCD digit!
What to do?
Try adding 6??

## Slide 9: BCD Operation (cont.)
Had 1010 and want to add 6 or 0110
  So 1 0 1 0
  plus 6 0 1 1 0
  Giving 1 0 0 0 0
Or a carry out to the next binary digit, or if the binary in BCD, the next BCD digit.

## Slide 10: BCD Operation (cont.)
Another carry example
Add 7 + 6
  have 7 0 1 1 1
  plus 6 0 1 1 0
  Giving 1 1 0 1 and again out of range
  Adding 6 0 1 1 0
  Giving 1 0 0 1 1 so a 1 carries out to the next BCD digit
  FINAL BCD answer 0001 0011 or 1310

## Slide 11: BCD Operation (cont.)
Multi Bit BCD
Add the BCD for 417 to 195 (Would expect to get 612)
BCD setup - start with Least Significant Digit
  417 0 1 0 0 0 0 0 1 0 1 1 1
  195 0 0 0 1 1 0 0 1 0 1 0 1
  1 1 0 0
  Adding 6 0 1 1 0
  Gives 1 0 0 1 0

## Slide 12: BCD Operation (cont.)
Multi Bit BCD
Had a carry to the 2nd BCD digit position
  1
  0 1 0 0 0 0 0 1 done
  0 0 0 1 1 0 0 1 0 0 1 0
  1 0 1 1
  Again must add 6 0 1 1 0
  Giving 1 0 0 0 1 And another carry

## Slide 13: BCD Operation (cont.)
Multi Bit BCD
Had a carry to the 3rd BCD digit position
  1
  0 1 0 0 done done
  0 0 0 1 0 0 0 1 0 0 1 0
  0 1 1 0
  And answer is 0110 0001 0010 or the BCD for the base 10 number 612

## Slide 14: Gray Code
When we count up or down in binary, the number of bit that change with each digit change varies.
  From 0 to 1 just have a single but
  From 1 to 2 have 2 bits, a 1 to 0 transition and a 0 to 1 transition
  From 7 to 8 have 3 bits changing back to 0 and 1 bit changing to a 1
For some applications multiple bit changes cause significant problems.

## Slide 15: Gray Code
Contrast of bit changes
Value | Binary | Number of bit change | Gray | Number of bit change
0 | 000 | --- | 000 | ---
1 | 001 | 1 | 001 | 1
2 | 010 | 2 | 011 | 1
3 | 011 | 1 | 010 | 1
4 | 100 | 3 | 110 | 1
5 | 101 | 1 | 111 | 1
6 | 110 | 2 | 101 | 1
7 | 111 | 1 | 100 | 1
0 | 000 | 3 | 000 | 1

## Slide 16: Binary to Gray Code Conversion Rule

## Slide 17: Binary to Gray Code Converter
Logic Design

## Slide 18: Gray to Binary Code Converter
Logic Design
4